## Slide 1
Model profile Magnet-Leakage

## Slide 2: Idea
Take raw data and cut it in time samples of e.g. 150 days. (Data of the two variables PHAP and helium level are taken into consideration at this time)
Helium level
phap
value
date
2021
2024
150 day time window
Day 0
Day 150
Embedding
Latent space
Embed this data in a latent low dimensonal space, so that similar data samples are close together. This is done by an (convolutional variational) autoencoder approach.

## Slide 3: Idea
Label a few samples by hand (leaking vs normal)
Latent space
2d projection of latent space
Train / Retrain semi-supervised model
(4. and 5. can be done iteratively)

## Slide 4: Input Data
Magnet Data: Feature Table (Pandas DF)
The example data contains the following:
Data from system 56005
Timepoint = „2024-05-27“
Values of the two variables helium_level and phap
A time-window of 160 days into the past
Normalisation:
        For helium_level: Subtraction of the mean value for this sample
        Standardscaler for each variable separatly

## Slide 5: Semi Supervised Variational Autoencoder Model
Input
( -1, 2, 150)
( -1, 128)
( -1, 64)
( -1, 32)
( -1, 16)
( -1, 8)
( -1, 128)
( -1, 64)
( -1, 32)
( -1, 16)
Reconstruction
( -1, 2, 150)
Latent space
Label
Encoder
Decoder
Classifier
The autoencoder is trained on all the data, and captures the structure of all the dataset
While training, the classifier adjusted to the few given labeled data samples. But it combines this knowledge with the structure of the dataset and is capable for making predictions on the whole dataset

## Slide 6
Dataflow
Feature table
Labels
Semi supervised model
t-SNE Visualization
Labeling tool
Helium loss prediction
Prepare features
Train and Predict

## Slide 7
Model demonstration
Spectra
Sempra
  - some issues with variance in data
  - helium loss not as obvious as in Spectra

## Slide 8
How to proceed
Integrate „pressure“-variable into model -> MICHAEL
Stabilize model for noisy data -> MICHAEL
Data-labeling using provided tool -> JAMES(DOMAIN EXPERT) + MICHAEL
Prepare final model report -> MICHAEL
Rollout of model and testing in real world scenario? New contract?